## Slide 1: Demand Driven Deployment Capabilities in Cyclus
Gwendolyn J. Chee1, Robert R. Flanagan2, Kathryn D. Huff1
1University of Illinois at Urbana-Champaign
2University of South Carolina
June 26, 2019
TwoFCS Workshop 2019

## Slide 2: Outline
Background
Motivation
D3ploy
Demonstrations
Conclusions

## Slide 3: CYCLUS
Agent-based framework [1]
Compatible with plug-in libraries
Gives users ability to customize agents
Agent types: facilities, institutions and regions
Discrete time steps
Background
Figure 1: Cyclus has a modular architecture [1]
Notes: A little bit about Cyclus for the people in the audience who are not too familiar. Cyclus is an agent based nuclear fuel cycle simulator
It is different from fleet based NFC simulators because every facility and isotope is individually tracked and not lumped.
As an agent based model, Cyclus has a modular architecture, and has plug-in libraries that are compatible with it. These plug in libraries give users the ability to give the simulator custom functionality. There is ease of creating independent agents for specific use without modifying core simulation. For example, a unique reactor archetype can be constructed and added into a fuel cycle simulation.
There are three kinds of agents: regions, institutions and facilities. Facilities are agents that manipulates materials EXAMPLES. An example is an enrichment facility, natural uranium enters and fresh uox fuel leaves the facility. Whereas Institutions control the deployment and decommissioning of facilities. And Regions represent countries or any geopolitical entities that the facilities and institutions are functioning in.
In this project, d3ploy is considered an institution agent since it controls the deployment of facilities in the simulation.
COMMUNICATION GOAL:
What is Cyclus

## Slide 4: Current fuel cycle simulators
w
Source
x
Enrichment
y
Reactor
z
Waste Storage
Energy demand growth: 1% / year
Background
?
Source
?
Enrichment
1
Reactor
?
Waste Storage
x kg
fuel
Figure 2: User defined Deployment Scheme
Figure 3: Demand Driven Deployment Scheme
Gap in capability: User must define when facilities are deployed
Bridging the gap: Developed demand-driven deployment capability in Cyclus, d3ploy.
Notes: Presently, in Cyclus it is up to the user to determine when each reactor and supporting facilities are deployed to meet current fuel cycle demand.
This means that if you have one reactor in your simulation and you know it is demanding x amount of fuel, it is up to user to determine how many source, enrichment and waste storage facilities have to be deployed to meet this demand.
However, having to do this is tedious and not optimal. It is simple for a scenario with only 1 reactor, however, it gets more complex if the demand changes over time and when there are many facilities are in play.
To overcome this, in this presentation we introduce the demand driven deployment capability in Cyclus, known as d3ploy.
D3ploy automatically deploys supporting fuel cycle facilities to meet demands of the fuel cycle.
And so for example if a user defines an energy demand growth of 1% per year, Cyclus will predict when to deploy reactor, enrichment ,source and waste storage facilities to automatically to meet this demand.
COMMUNICATION GOAL:
Fuel cycle simulators are not demand driven but require user defining the deployment.

## Slide 5: D3ploy -- Input Options
D3ploy
Table 1: D3ploy Input Parameters
Notes: This is the input parameters for d3ploy. Go through each input option.
I will give an example scenario and the resulting plots are on the next slide.

## Slide 6: D3ploy – Logic Flow
Figure 3: D3ploy logic flow
D3ploy
Notes: D3ploy’s primary objective is minimizing the number of time steps in which there is an undersupply of any commodity.
At each time step, d3ploy will predict the demand and supply of a commodity for the next time step.
If it predicts an undersupply, it responds by deploying the fewest number of available facilities to meet demand with minimal oversupply. This will be repeated for all commodities that are controlled by that d3ploy institution. After all that is done, it will move on to the next time step.

## Slide 7: Prediction Methods
Non-Optimizing Methods
  Demand Response
  Moving Average
  Autoregressive Moving Average
  Autoregressive Heteroskedasticity
Deterministic Methods
  Fast Fourier Transform
  Polynomial Fit
  Exponential Smoothing and Holt-Winters
Matrix Solution
  Uses supply and demand to create a system of equations in matrix form.
  Solving the matrix returns the number of facilities required at a given time-step.

## Slide 8: D3ploy -- Input Options
D3ploy
Table 2: D3ploy Input Parameters with example
Notes: This is the input parameters for d3ploy. Go through each input option.
I will give an example scenario and the resulting plots are on the next slide.

## Slide 9: Constant Power Demand
Demonstrations
Figure 4: Power commodity supply and demand for transition scenario of constant 10000MW power demand
Notes: In this simple transition scenario, we initially have 10 reactors that meet the 10000MW power demand. At time step 40, they start to decommission. This is where d3ploy comes in to meet the power demand. D3ploy begins to deploy newreactor facilities to meet the gap in power supply to ensure that the power demand is met for all time steps. By using a combination of the fast fourier transform method for predicting demand and setting the supply buffer to 3000MW (the capacity of 3 reactors), the simulation does not under supply power. The red T’s refer to demand and the blue crosses supply.

## Slide 10: Constant Power Demand
Demonstrations
Figure 5: Fuel commodity supply and demand for transition scenario of constant 10000MW power demand
Figure 6: Spent Fuel commodity supply and demand for transition scenario of constant 10000MW power demand
Notes: These figures show the demand and supply for fuel and spent fuel.

## Slide 11: Linear Power Demand
Demonstrations
Figure 7: Power commodity supply and demand for transition scenario of linearly increasing power demand

## Slide 12: Sinusoidal Power Demand
Demonstrations
Figure 8: Power commodity supply and demand for transition scenario of sinusoidal power demand

## Slide 13: Conclusions
Conclusions
Demand driven deployment capabilities in Cyclus are important to automate setting up of transition scenarios.
Future Work: Similar power demand transition scenarios extended to include more nuclear fuel cycle facilities such as reprocessing facilities etc.

## Slide 14: References
[1]: K. D. HUFF, M. J. GIDDEN, R. W. CARLSEN, R. R. FLANAGAN, M. B.
MCGARRY, A. C. OPOTOWSKY, E. A. SCHNEIDER, A. M. SCOPATZ, and
P. P. H. WILSON, “Fundamental concepts in the Cyclus nuclear fuel cycle
simulation framework,” Advances in Engineering Software, 94, 46–59 (Apr.
2016).
Notes: 1414

## Slide 15: Acknowledgements
This work is supported by U.S. Department of Energy, Nuclear Energy University Program, under contract # NEUP- FY16-10512.

## Slide 16: Thank You Any Questions?